## Slide 1: USM3D-ME Simulations for DPW-VII: Expanding the Envelope
Brent Pomeroy Mohagna Pandya NASA Langley Research Center Configuration Aerodynamics Branch | Boris Diskin National Institute of Aerospace
Taylor Kate Boyett NASA Langley Research Center Intern, Configuration Aerodynamics Branch Senior, Georgia Institute of Technology | 
CFD Drag Prediction Workshop VII: Expanding the Envelope 2022 AIAA Aviation Forum June 25-26, 2022 | 

## Slide 2: Outline
USM3D-ME Overview
Grids and Computational Methodology
Selected Cases
  Case 1a: Grid Convergence Study for Re=20 million
  Case 2a: Alpha Sweep for Re=20 million
  Case 3: Reynolds Number Sweep

## Slide 3: USM3D-ME (TetrUSS Flow Solver)
Builds on rich legacy of USM3D tetrahedral grid flow solver
Cell-centered, finite-volume, mixed-element, unstructured-grid flow solver
  Euler and RANS equations with second-order spatial accuracy
  Spalart-Allmaras (SA) turbulence model (standard, negative, RC, and QCR2000)
Upwind spatial discretization for mean flow inviscid flux
  Cell gradients using Green-Gauss method and nodal solutions
  Options for flux functions: FDS, HLLC, LDFSS, FVS, HLLE, etc.
  Cell- and face-based gradient limiters: Barth-Jespersen, Venkat, van Albada
Second-order diffusion; face-gradients based on Mitchell’s method
P3-Orion
Courtesy Craig Hunter (NASA LaRC)

## Slide 4: USM3D-ME (TetrUSS Flow Solver)
Standard and specialized boundary conditions
Force-term approach for simulation of propellers and other applications
Time integration
  Steady state with local time-stepping
  Second-order BDF2 for temporal accuracy
Rigid-body 6-DoF motion support
Parallelized using MPI paradigm; excellent scalability
Nonlinear iteration methods
  Preconditioner-Alone (PA); baseline solver technology
  Hierarchical Adaptive Nonlinear Iteration Method (HANIM); stronger solver for improved robustness and efficiency; automatic update of CFL
  AIAA 2013-2541, AIAA Journal, 54(9) 2016, AIAA Journal, 55(10) 2017, AIAA 2019-2333,
  AIAA Journal, 59(8) 2021, AIAA Journal, 59(11) 2021
CRM Wing/Body

## Slide 5: Compute Resources
NASA Advanced Supercomputing (NAS) facility
Located at NASA Ames Research Center
  More than 11,000 nodes and 241,000 compute cores
  Intel and AMD chips
  TOSS3 operating system
Resource usage for DPW-VII
  IvyBridge (Intel) chips
  Between 600 and 2,500 processors
  Medium cases run on 600 processors
  Walltime totaled a few hours, depending on the grid and convergence criteria

## Slide 6: Grids
Used mixed-element JAXA-supplied grids
  Grid convergence study performed on all six grids
  Majority of work executed on medium-density grid
  Nondimensionalized by mean aerodynamic chord
Aeroelastic deformations incorporated in grids
Tiny
Ultra Fine
 | Tiny | Coarse | Medium | Fine | Extra Fine | Ultra Fine
Level | L1 | L2 | L3 | L4 | L5 | L6
Approximate Cell Count (Millions) | 8.7 | 26.9 | 60.2 | 111.8 | 184.1 | 291.2

## Slide 7: Computational Approach
RANS scheme for all simulations
Turbulence model
  SA-neg QCR-2000
  RC not utilized as best practices have not yet been established
  First-order advection term
Inviscid flux for meanflow equations
  Second-order
  Roe’s flux different splitting scheme without gradient limiters

## Slide 8: Case 1a: Grid Convergence
Simulations performed on all six grids
  Rapid iterative convergence from HANIM methodology
  Solution residuals reduced below 1.0E-13
Solution value taken at final iteration
Simulations performed in CL-matching mode
  Tolerance for CL set at committee-specified +- 0.0001
  Angle of attack perturbed automatically to match prescribed CL within the tolerance limits
  Angle of attack adjusted after residuals are reduced 1.5 orders of magnitude below the initial freestream state
(deg.)

## Slide 9: Case 1a: Convergence History
Convergence history monitored and stopped by the user
Drag has converged within six significant digits for all cases

## Slide 10: Case 1a: Medium and Ultra Fine Grids

## Slide 11: Case 2a: Iterative Convergence
Solution residuals reduced below 1.0E-13
Low-alpha cases converged in ~1k iterations
Converged solutions observed after 5k iterations for all simulations
deg.
deg.
deg.
deg.
deg.
deg.
deg.

## Slide 12: Case 2a: Aerodynamic Performance
Pitch break observed between CL of ~0.62 and ~0.65 (3 to 3.25 deg.)
Bucket of pitching moment curve at CM of about –0.133
(deg.)

## Slide 13: Case 2a: Surface Separation Behavior
Surface contours of CF with streamlines
Shock-induced separation observed at 3.00 deg.
Midspan separation seen at 3.25 deg. (consistent with pitch break)
CL = 0.618
Alpha = 3.00 deg.
CL = 0.583
Alpha = 2.75 deg.
CL = 0.645
Alpha = 3.25 deg.
Significant
separation
Moderate
separation

## Slide 14: Case 2a: Inboard Surface Cuts
Cuts shown for the fixed-alpha conditions
Attached flow present across all simulations
Consistent with previous contour plots

## Slide 15: Case 2a: Mid-Span Surface Cuts
Region of earliest separation
Extent of downstream separation increases with larger alphas
Trailing edge flow separation for alpha above 3.00 deg.

## Slide 16: Case 3: Reynolds Number Sweep
Significant increase in drag for decreasing Reynolds number as the wing moves off design
Deviations in CM ~0.016 between two 20 million cases (different conditions and lofts)
𝛼 (deg.)

## Slide 17: Case 3: Surface Pressure Comparison
Spanwise flow observed for low-Reynolds number case
Re = 5 million
Re = 30 million
Midspan spanwise flow

## Slide 18: Conclusions
USM3D-ME results for cases 1a, 2a, and 3 presented
Rapid convergence to machine-zero residuals achieved (less than 1,000 iterations for some cases)
Strong grid convergence across all six JAXA grids
Pitch break at CL ~0.62 (alpha ~3.15 deg.)
Committee-required data files previously provided

## Slide 19: Acknowledgments
NAS for compute facilities
Appreciation extended to the DPW-7 workshop committee for providing grids, the data format, and data reduction scripts