## Slide 1: OVERFLOW & GGNS-T1 Analysis of the NASA CRM WB configuration for DPW-VII
Ben Rider Boeing Commercial Airplane
Dmitry Kamenetskiy Boeing Research & Technology
Behzad Reza Ahrabi Boeing Research & Technology
Joshua Krakos Boeing Research & Technology

## Slide 2: Outline
Flow Solvers and Grid Summary
  OVERFLOW (NASA)
  GGNS-T1 (Boeing)
Convergence History
Cases Analyzed
  OVERFLOW
  GGNS-T1
Results
  Case 1: CRM Wing-Body Grid Convergence Study
  Case 2: CRM Wing-Body Alpha Sweep
  Case 3: CRM Wing-Body Reynolds Number Sweep At Constant CL
  Case 4: CRM Wing-Body Alpha Sweep with Grid Adaptation
Conclusions

## Slide 3: OVERFLOW: Solver, Grid and Computing Platform
OVERFLOW version 2.3e
Same setup as used for past workshops for consistency
  2nd order central differencing
    Central / Beam-Warming scalar pentadiagonal scheme (IRHS=0, ILHS=2)
  SA turbulence model (SA-neg-noft2) with:
    RC: rotation/curvature corrections
    QCR: nonlinear stress model via QCR
  fully turbulent boundary layer, free stream initial conditions
  full N-S, exact wall distance calculation
Common Overset Grid
  Provided by Committee
Utilized Ivy Bridge nodes with 2 ten-core processor per node
case | grid | points (M) | cores | sec/it | sec/it/grid | iterations | wall clock
T | Tiny | 5.72 M | 40 | 0.94 | 16.550e-8 | 20000 | 5.1 hrs
C | Coarse | 18.62 M | 40 | 1.95 | 10.450e-8 | 20000 | 10.5 hrs
M | Medium | 43.32 M | 120 | 1.60 | 3.703e-8 | 25000 | 10.9 hrs
F | Fine | 83.66 M | 220 | 2.10 | 2.511e-8 | 25000 | 14.3 hrs
X | Extra Fine | 143.47 M | 300 | 2.28 | 1.599e-8 | 30000 | 18.8 hrs
U | Ultra Fine | 226.59 M | 460 | 2.79 | 1.240e-8 | 35000 | 26.9 hrs

## Slide 4: GGNS-T1: Solver, Grid and Computing Platform
GGNS-T1
Discretization
  SU/PG(1)
    Tetrahedral cells
    piecewise-linear, globally continuous finite elements
    Residual-based stabilization
  Shock capturing/artificial dissipation by (Glasby et.al.[1])
Solver
  RANS, steady-state (SA, SA-QCR2000, SARC-QCR2000 fully turbulent)
  Fully coupled turbulence equations
  Exact Jacobians (except SARC) with operator overloading
  Pseudo-transient continuation to steady-state
  Newton’s method
  Parallel MPI implementation based on PETSc [2]
  12 orders for the dual-volume weighted discrete residuals
  10 orders for the adjoint linear system residual
Adaptation : EPIC [3]
  Goal oriented (GO) “ε1+ ε2, multi-component” from [4]
400 cores x 24 hours for 24 solver/adaptation cycles
  Includes primal and adjoint solves and grid adaptation times
case | grid | points (M)
- | L0 – L13 | 0 –> 1.8 M
- | L14 – L16 | ~3.6 M
- | L17 | ~5.0 M
- | L18 - L20 | ~6.8 M
- | L21 | ~10.9 M
- | L22 – L24 | ~13.5 M
EPIC Adapted Grids
Drag Adjoint Adaption

## Slide 5: GGNS-T1/EPIC Grid Visualization

## Slide 6: Convergence History: Residuals
Residuals for Mach 0.85, CL = 0.58
  Medium Grid
OVERFLOW
Rey# 20M
Rey# 5M
GGNS-T1
(Final Grid)

## Slide 7: Convergence History: Force/Moment
Forces/Moments for Mach=0.85, CL=0.58
Drag Coefficient
Pitching Moment

## Slide 8: Cases Analyzed
Case 1: Grid Convergence Study (CL=0.58) | OVERFLOW | GGNS-T1
Case 1a: Rey# 20M | X | X
Case 1b: Rey# 5M | X | X
Case 2: Alpha Sweep (Fixed Grid) | OVERFLOW | GGNS-T1
Case 2a: Rey# 20M | X | X
Case 2b: Rey# 5M | X | X
Case 3: Reynolds Number / Q Sweep | OVERFLOW | GGNS-T1
Case 3: CL=0.50 | X | X
Case 4: Alpha Sweep (Grid Adaptive) | OVERFLOW | GGNS-T1
Case 4a: Rey# 20M |  | X
Case 4b: Rey# 5M |  | X

## Slide 9: Case 1
CRM Wing-Body Grid Convergence Study

## Slide 10: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
SA-QCR
 Increasing Grid Size
 Increasing Grid Size
Total Drag
Angle of Attack
20 cnts
0.1°

## Slide 11: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
SA (no QCR)
SA-QCR
 Increasing Grid Size
Rey# 5M
Rey# 20M
Rey# 5M
Rey# 20M
spurious side-of-body
juncture separation!
 Increasing Grid Size
Total Drag
Angle of Attack
20 cnts
0.1°

## Slide 12: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
SA (no QCR)
SA-QCR
 Increasing Grid Size
Rey# 5M
Rey# 20M
Rey# 5M
Rey# 20M
spurious side-of-body
juncture separation!
 Increasing Grid Size
Total Drag
Angle of Attack
SA (no QCR) will be
ignored on remainder
of Case 1 charts
20 cnts
0.1°

## Slide 13: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
 Increasing Grid Size
 Increasing Grid Size
Total Drag
Angle of Attack
10 cnts
0.1°

## Slide 14: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
 Increasing Grid Size
 Increasing Grid Size
Pressure Drag
Viscous Drag
10 cnts
5 cnts

## Slide 15: Case 1: CRM Wing-Body Grid Convergence Study
Case 1a: Mach=0.85, CL=0.58, Rey# 20M
  Closed Symbols
Case 1b: Mach=0.85, CL=0.58, Rey# 5M
  Open Symbols
 Increasing Grid Size
Pitching Moment
Pressure Comparison (CL=0.58, Rey# 20M)
  Section 12 – Eta = 0.7268

## Slide 16: Case 1: CRM Wing-Body Grid Convergence Study
Pressure comparison: Section 12 – Eta = 0.7268
  CL=0.58, Rey# 20M

## Slide 17: Case 1: CRM Wing-Body Grid Convergence Study
Spanload comparison
  CL=0.58, Rey# 20M

## Slide 18: Case 1: CRM Wing-Body Grid Convergence Study
Sectional Moment comparison
  CL=0.58, Rey# 20M

## Slide 19: Case 2
CRM Wing-Body Alpha Sweep

## Slide 20: CRM Wing-Body Alpha Sweep
Case 2a: Mach=0.85, Rey# 20M, Alpha=[2.75° - 4.25° by 0.25°]
  Closed Symbols
Case 2b: Mach=0.85, Rey# 5M, Alpha=[2.75° - 4.25° by 0.25°]
  Open Symbols
Drag Polar
Lift Polar
50 cnts
0.5°

## Slide 21: Case 2: CRM Wing-Body Alpha Sweep
Case 2a: Mach=0.85, Rey# 20M, Alpha=[2.75° - 4.25° by 0.25°]
  Closed Symbols
Case 2b: Mach=0.85, Rey# 5M, Alpha=[2.75° - 4.25° by 0.25°]
  Open Symbols
Pressure Drag Polar
Viscous Drag Polar
50 cnts
10 cnts

## Slide 22: Case 2: CRM Wing-Body Alpha Sweep
Case 2a: Mach=0.85, Rey# 20M, Alpha=[2.75° - 4.25° by 0.25°]
  Closed Symbols
Case 2b: Mach=0.85, Rey# 5M, Alpha=[2.75° - 4.25° by 0.25°]
  Open Symbols
Pitching Moment vs. CL
Pitching Moment vs Alpha

## Slide 23: Case 2: CRM Wing-Body Alpha Sweep
Case 2a: Mach=0.85, Rey# 20M, Alpha=[2.75° - 4.25° by 0.25°]
  Closed Symbols
Case 2b: Mach=0.85, Rey# 5M, Alpha=[2.75° - 4.25° by 0.25°]
  Open Symbols
Rey# 20M: Trailing Edge Separation
Rey# 5M: Trailing Edge Separation
No TE
Separation

## Slide 24: Case 2: CRM Wing-Body Alpha Sweep
Spanload comparison

## Slide 25: Case 2: CRM Wing-Body Alpha Sweep
Spanload comparison

## Slide 26: Case 3
Wing-Body Reynolds Number Sweep At Constant CL
  CL=0.50, Mach=0.85, LoQ, Rey# 5M
  CL=0.50, Mach=0.85, LoQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 30M
AIAA-2008-6919, Vassberg, et al. “Development of a Common Research Model for Applied CFD Validation Studies”

## Slide 27: Case 3: Wing-Body Reynolds # Sweep At Constant CL=0.50
Case 3:
  CL=0.50, Mach=0.85, LoQ, Rey# 5M
  CL=0.50, Mach=0.85, LoQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 30M
CDideal
Pitching Moment
Angle of Attack
NTF197 & NTF215
Test Data +/- sigma
AIAA 2012-0707, M. Rivers and C. Hunter “Support System Effects on the NASA Common Research Model”
AIAA 2012-3209, M. Rivers, C. Hunter, and R. Campbell “Further Investigation of the Support System Effects and Wing Twist on the NASA Common Research Model”
Adding the model support system to the CFD model changes wing, tail and aft body pressures and increases CM by ~0.03 and α by ~0.2° at CL = 0.50 for the Wing-Body-Tail configuration

## Slide 28: Case 3: Wing-Body Reynolds # Sweep At Constant CL=0.50
Case 3:
  CL=0.50, Mach=0.85, LoQ, Rey# 5M
  CL=0.50, Mach=0.85, LoQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 20M
  CL=0.50, Mach=0.85, HiQ, Rey# 30M
CDideal
Pitching Moment
Angle of Attack
AIAA 2012-0707, M. Rivers and C. Hunter “Support System Effects on the NASA Common Research Model”
AIAA 2012-3209, M. Rivers, C. Hunter, and R. Campbell “Further Investigation of the Support System Effects and Wing Twist on the NASA Common Research Model”
Adding the model support system to the CFD model changes wing, tail and aft body pressures and increases CM by ~0.03 and α by ~0.2° at CL = 0.50 for the Wing-Body-Tail configuration
NTF197 & NTF215
Test Data +/- sigma

## Slide 29: Case 4
CRM Wing-Body Alpha Sweep with Grid Adaptation

## Slide 30: Case 4: CRM Wing-Body Alpha Sweep with Grid Adaptation
Case 4a: Mach=0.85, Rey# 20M, Alpha=[2.75° - 4.25° by 0.25°]
  Closed Symbols
Case 4b: Mach=0.85, Rey# 5M, Alpha=[2.75° - 4.25° by 0.25°]
  Open Symbols
Rey# 20M: Drag Polar
Rey# 5M: Drag Polar
50 cnts

## Slide 31: Conclusions
Solver Comparison
  The agreement between very different grid and solver strategies is very impressive
Turbulence Model
  SA without QCR results in non-physical side-of-body separation
    Consistent with previous DPW results
  RC terms have an impact on forces/moments
    Reduced lift and more positive pitching moment at constant alpha
Grid Adaption
  GGNS-T1 with EPIC adaption based on the drag adjoint achieves results for Lift, Drag, and Pitching Moment comparable to OVERFLOW on the L6-UltraFine grid with an order of magnitude smaller grid!
    Overflow L6: 226.6M
    GGNS-T1 L24: ~13M
  Alternative grid adaption based on flow features and/or the lift adjoint based metrics converge to the same result as the those shown here based on the drag adjoint.

## Slide 33: References
[1] K R Holst, R S Glasby, J T Erwin, D L Stefanski, J G Coder, High-Order Shock Capturing Techniques using HPCMP CREATE-AV Kestrel, AIAA Scitech 2019 Forum, 2019
[2] https://petsc.org
[3] Todd Michal and Joshua Krakos, Anisotropic Mesh Adaptation Through Edge Primitive Operations, AIAA Paper 2012--159
[4] Dmitry S. Kamenetskiy, Joshua A. Krakos, Todd Michal, Francesco Clerici, Frédéric Alauzet, Adrien Loseille, Michael A. Park, Stephen L. Wood, Aravind Balan, Marshall C. Galbraith, Anisotropic Goal-Based Mesh Adaptation Metric Clarification and Development, AIAA paper 2022-1245