## Slide 1: 7th AIAA Drag Prediction Workshop Metacomp Technologies, Inc.
AIAA Aviation 2022
Chicago, IL 25-26 June 2022
Nili Bachchan
Paul Batten
Ravi Kovvali
Oshin Peroomian
Amar Potturi
Beerinder Singh

## Slide 2: Overview
Solver, settings & models
Case 1a: Grid Convergence Study
Case 2a: Alpha Sweep (Re=20M)
Case 3: Re sweep (CL=0.50)
Case 6: Coupled aero-structural
Summary

## Slide 3
CFD++ Version 20.1
Bounded nodal-reconstruction transport
HLLC Riemann solver
Self-tuning far-field absorbing layers
Implicit solver with algebraic multi-grid acceleration
CL-driver option (for imposed CL cases)
SARC+QCR2013 and SST models
Solver & Settings

## Slide 4
6 Simulations performed – one with each grid from the JAXA hybrid mesh family: tiny, coarse, medium, fine, extra fine and ultra fine
CFD++’s CL-driver used to automatically adjust the angle-of-attack to achieve desired CL = 0.58 (± 0.0001)
Case 1a: Grid Convergence Study

## Slide 5
JAXA hybrid mesh family with tetrahedrals, pyramids, prisms, and hexahedrals
Grid Level | # Cells
Tiny | 25,294,690
Coarse | 76,058,884
Medium | 164,065,758
Fine | 295,240,476
Extra fine | 476,358,610
Ultra fine | 739,171,907
Grids

## Slide 6
Tiny
Medium
Ultra Fine
Sample Residual Convergence

## Slide 7
CL History

## Slide 8
α History

## Slide 9
α History (Zoomed-in)

## Slide 10
Grid Convergence

## Slide 11
Case 2a : Wing-Body Alpha Sweep
α=2.75˚Cl =0.580000 SARC-QCR

## Slide 12
Case 2a : Wing-Body Alpha Sweep
α=2.75˚Cl =0.580000 SARC-QCR

## Slide 13
Flow conditions: Mach 0.85, Re=20M, Ttotal= -250˚F
CFD++ Compressible RANS (Air, Perfect Gas)
Case 2a : Wing-Body Alpha Sweep
α | Mesh
2.23˚ (CL=0.50) | 2.50˚ LoQ JAXA Medium
2.75˚ | 2.75˚ LoQ JAXA Medium
3.00˚ | 3.00˚ LoQ JAXA Medium
3.25˚ | 3.25˚ LoQ JAXA Medium
3.50˚ | 3.50˚ LoQ JAXA Medium
3.75˚ | 3.75˚ LoQ JAXA Medium
4.00˚ | 4.00˚ LoQ JAXA Medium
4.25˚ | 4.25˚ LoQ JAXA Medium

## Slide 14
Residuals: α = 2.50˚ (CL-driver active)
Notes: OLD

## Slide 15
Alpha-Sweep Residuals: SARC+QCR, Re=4M
α = 2.75˚
α = 3.00˚
α = 3.25˚
α = 3.50˚
α = 3.75˚
α = 4.00˚
Notes: OLD

## Slide 16
Alpha-Sweep Residuals: SST, Re=4M
α = 2.75˚
α = 3.00˚
α = 3.25˚
α = 3.50˚
α = 3.75˚
α = 4.00˚
Notes: OLD

## Slide 17
Cross-Section Mach Contours and Separation Re=4M
Isosurface Comparisons
α=4.00˚: SARC-QCR (Left) and SST/Start Soln nt=8900 (Right)
Aircraft surface: Pressure
Isosurface: -1 m/s x-velocity component
Cutplane: Mach number

## Slide 18
α=4.00˚: SARC-QCR (Left) and SST/Cont Soln nt=14200 (Right)
Aircraft surface: Pressure
Isosurface: -1 m/s x-velocity component
Cutplane: Mach number
Cross-Section Mach Contours and Separation Re=4M
Isosurface Comparisons

## Slide 19
Alpha-Sweep Residuals: SARC+QCR, Re=20M
α = 2.75˚
α = 4.25˚
Notes: OLD

## Slide 20
α | CL | CD
2.23˚ | 0.50 | 0.022517
2.75˚ | 0.577272 | 0.027241
3.00˚ | 0.609559 | 0.030213
3.25˚ | 0.633715 | 0.033557
3.50˚ | 0.651930 | 0.038059
3.75˚ | 0.669637 | 0.041414
4.00˚ | 0.686953 | 0.045781
4.25˚ | 0.703539 | 0.050348
Shock-induced separation from 2.75˚
Side-of-body separation in all cases
Case 2a : Wing-Body Alpha Sweep

## Slide 21
Drag Components
Wing/Body Contribution
Case 2a : Wing-Body Alpha Sweep

## Slide 22
Drag Coefficient
Case 2a : Wing-Body Alpha Sweep
No sting correction applied to NTF data

## Slide 23
No sting correction applied to NTF data
Case 2a : Wing-Body Alpha Sweep
Lift Coefficient

## Slide 24
Pitching Moment Coefficient
Corrections applied to NTF tunnel data:
Model blockage
Wake blockage
Tunnel buoyancy
Lift interference
Case 2a : Wing-Body Alpha Sweep
No sting correction applied to NTF data

## Slide 25
Many tunnel installation effects can cause a shift:
Error in true alpha measurement
Error in moment-center offset
Model/mount aeroelastic effects
Unknown effects of tunnel corrections
Case 2a : Wing-Body Alpha Sweep
No sting correction applied to NTF data
CM vs CL

## Slide 26
CM vs CL – with shift in CM
Case 2a : Wing-Body Alpha Sweep
No sting correction applied to NTF data

## Slide 27
Re: 4 million
Mach 0.85
T = -250˚ F
Angle-of-Attack Sweep from 2.50˚ to 4.25˚
Case 2a : Wing-Body Alpha Sweep
No sting correction applied to NTF data
CM vs CL – with shift in CM
Test-NTF : (Re 5M)
Test-Ames : (Re 5M)
Notes: Presumably this good agreement is a bit fortuitous, because this NTF data also wouldn’t have a sting correction applied?

## Slide 28
Case 2a : Wing-Body Alpha Sweep
α=2.75˚SARC-QCR
α=4.25˚SARC-QCR

## Slide 29
Case 2a : Wing-Body Alpha Sweep
α=2.75˚SARC-QCR
α=4.25˚SARC-QCR

## Slide 30
Reynolds Sweep at Constant Cl=0.50 and Mach 0.85
Medium JAXA grids
CFD++ Compressible RANS (Air, Perfect Gas)
Turbulence Model: SARC-QCR
All simulations run with CL-driver
Reynolds # | Pstatic (kPa) | Tstatic (˚K) | U∞ (m/s) | q (kPa)
5M LoQ | 125 | 271.67 | 280.92 | 63
20M LoQ | 127 | 101.77 | 171.94 | 64
20M HiQ | 192 | 134.78 | 197.87 | 97
30M HiQ | 189 | 101.78 | 171.94 | 96
Case 3 : Reynolds Number Sweep (CL=0.50)

## Slide 31
No shock induced separation in all cases
Angles-of-attack settle below 2.45˚
Case 3 : Reynolds Number Effects
Reynolds # | CL | α
5M LoQ | 0.50 | 2.4495˚
20M LoQ | 0.50 | 2.2314˚
20M HiQ | 0.50 | 2.4046˚
30M HiQ | 0.50 | 2.3489˚

## Slide 32
Drag Coefficient
Pitching Moment Coefficient
Case 3 : Reynolds Number Effects
N.B. 5millionLoQ CFD Q=1325 / NTF Run 44 Q=1388
20millionLoQ CFD Q=1338 / NTF Run 250 Q=1313
20millionHiQ CFD Q=2031 / NTF Run 159 Q=1988
30millionHiQ CFD Q=2007 / NTF Run 146 Q=1989
Alphas are approximate and no sting correction applied to NTF data
&

## Slide 33: Misc. Observations 1 #1: TE (Shock) & SOB/Wing Separations
SOB separation in terms of vortex eye on body…
… and shock-induced separation location: Both unambiguous for all cases
In most cases wing separation is more complicated…

## Slide 34: Which Vortex Eye Do We Want?
λ2 isosurface
Q-criterion isosurface

## Slide 35: Which Vortex Eye Do We Want?
λ2 /Q-criterion isosurfaces:

## Slide 36: Which Vortex Eye Do We Want?
Surface and volume streamlines

## Slide 37: Case 1a : Juncture-Region SOB Separation

## Slide 38: Case 1a : Juncture-Region SOB Separation
SOB separation: Tiny mesh

## Slide 39: Case 1a : Juncture-Region SOB Separation
SOB separation: Coarse mesh

## Slide 40: Case 1a : Juncture-Region SOB Separation
SOB separation: Medium mesh

## Slide 41: Case 1a : Juncture-Region SOB Separation
SOB separation: Fine mesh

## Slide 42: Case 1a : Juncture-Region SOB Separation
SOB separation: Extra Fine mesh

## Slide 43: Case 1a : Juncture-Region SOB Separation
SOB separation: Ultra Fine mesh

## Slide 44: Case 1a : Juncture-Region Wing Separation

## Slide 45: Case 1a : Juncture-Region Wing Separation
Wing separation: Tiny mesh

## Slide 46: Case 1a : Juncture-Region Wing Separation
Wing separation: Coarse mesh

## Slide 47: Case 1a : Juncture-Region Wing Separation
Wing separation: Medium mesh

## Slide 48: Case 1a : Juncture-Region Wing Separation
Wing separation: Fine mesh

## Slide 49: Case 1a : Juncture-Region Wing Separation
Wing separation: Extra Fine mesh

## Slide 50: Case 1a : Juncture-Region Wing Separation
Wing separation: Ultra Fine mesh

## Slide 51: Case 1a : Juncture-Region Mesh
Tiny mesh

## Slide 52: Case 1a : Juncture-Region Mesh
Coarse mesh

## Slide 53: Case 1a : Juncture-Region Mesh
Medium mesh

## Slide 54: Case 1a : Juncture-Region Mesh
Fine mesh

## Slide 55: Case 1a : Juncture-Region Mesh
ExtraFine mesh

## Slide 56: Case 1a : Juncture-Region Mesh
UltraFine mesh

## Slide 57: Case 1a : Juncture-Region Mesh
UltraFine mesh + surface srteamlines

## Slide 58: Case 2a : Juncture-Region Wing Separation

## Slide 59: Case 2a : Juncture-Region Wing Separation
Wing separation: CL=0.50 2.50˚ LoQ AE CRM geometry

## Slide 60: Case 2a : Juncture-Region Wing Separation
Wing separation: α=2.75˚ 2.75˚ LoQ AE CRM geometry

## Slide 61: Case 2a : Juncture-Region Wing Separation
Wing separation: α=3.00˚ 3.00˚ LoQ AE CRM geometry

## Slide 62: Case 2a : Juncture-Region Wing Separation
Wing separation: α=3.25˚ 3.25˚ LoQ AE CRM geometry

## Slide 63: Case 2a : Juncture-Region Wing Separation
Wing separation: α=3.50˚ 3.50˚ LoQ AE CRM geometry

## Slide 64: Case 2a : Juncture-Region Wing Separation
Wing separation: α=3.75˚ 3.75˚ LoQ AE CRM geometry

## Slide 65: Case 2a : Juncture-Region Wing Separation
Wing separation: α=4.00˚ 4.00˚ LoQ AE CRM geometry

## Slide 66: Case 2a : Juncture-Region Wing Separation
Wing separation: α=4.25˚ 4.25˚ LoQ AE CRM geometry

## Slide 67: Case 3 : Juncture-Region Wing Separation

## Slide 68: Case 3 : Juncture-Region Wing Separation
Wing separation: Re=5M, CL=0.50 2.50˚ LoQ AE CRM geometry

## Slide 69: Case 3 : Juncture-Region Wing Separation
Wing separation: Re=20M, CL=0.50* 2.50˚ LoQ AE CRM geometry *(same as Case 2a, CL=0.50)

## Slide 70: Case 3 : Juncture-Region Wing Separation
Wing separation: Re=20M, CL=0.50 2.50˚ HiQ AE CRM geometry

## Slide 71: Case 3 : Juncture-Region Wing Separation
Wing separation: Re=30M, CL=0.50 2.50˚ HiQ AE CRM geometry

## Slide 72: Case 6 : Juncture-Region Wing Separation

## Slide 73: Case 6 : Juncture-Region Wing Separation
Wing separation: CL=0.58
q/E=0.334 x10-6

## Slide 74: Case 6 : Juncture-Region Wing Separation
Wing separation: α=3.25˚
q/E=0.334 x10-6

## Slide 75: Case 6 : Juncture-Region Wing Separation
Wing separation: α=3.50˚
q/E=0.334 x10-6

## Slide 76: Case 6 : Juncture-Region Wing Separation
Wing separation: α=3.75˚
q/E=0.334 x10-6

## Slide 77: Case 6 : Juncture-Region Wing Separation
Wing separation: α=4.00˚
q/E=0.334 x10-6

## Slide 78: Case 6 : Juncture-Region Wing Separation
Wing separation: α=4.25˚
q/E=0.334 x10-6

## Slide 79: Misc. Observations 2 #2: Confirmation of Sectional-Integration Macro
Latest version of Tecplot sectional-integration macro agrees with the built-in sectional integration tool in CFD++
Tecplot macro #3
Direct CFD++ sectional-integration probe

## Slide 80
FSI
CSM++
CFD++
MetaFSI
CFD++ is coupled with Metacomp’s software suite designed for Fluid-Structure Interaction:
  CSM++ : An in-house finite-element based structural mechanics and dynamics package
  MetaFSI: A suite of tools designed to
    Transfer loads from CFD++ to CSM++
    Morph the CFD++ mesh based on structural displacements
Case 6 : Coupled Aero-Structural
Simulation

## Slide 81
FE Model: Eigenvalue Analysis
Start with the FE model for wing/body/tail=0˚ configuration from NASA CRM website
Create a wing/body configuration by removing all elements making up the horizontal tail
Import NASTRAN model in to CSM++ and run modal analysis for both configurations
Compare frequencies and mode shapes from CSM++ with Prof. Mavriplis’ results (Abaqus)
Mode # | CSM++ (Wing/Body) | CSM++ (Wing/Body/Tail=0˚) | Prof. Mavriplis
1 | 38.157 Hz (-3.06%) | 38.147 Hz (-3.08%) | 39.360 Hz
2 | 39.561 Hz (-3.37 %) | 39.535 Hz (-3.44 %) | 40.942 Hz
Notes: Talk about asymmetry

## Slide 82
Flow conditions: Mach 0.85, Re=20M, Ttotal=116˚ K
Default value of Young’s Modulus of the wing in FEM Model: E = 1.827x1011 N/m2
This resulted in a q/E of 0.351, higher than the intended q/E of 0.334!
Young’s Modulus adjusted to E = 1.918x1011 N/m2 to match test case definition
FE Model: Adjusted Eigenvalue Analysis
Mode # | CSM++ (Wing/Body) | CSM++ (Wing/Body/Tail=0˚) | Prof. Mavriplis
1 | 38.991 Hz (-0.94%) | 38.979 Hz (-0.97%) | 39.360 Hz
2 | 40.432 Hz (-1.25%) | 39.535 Hz (-1.32%) | 40.942 Hz
Notes: Talk about unclear Ttotal (maybe), and unclear q/E (maybe). Primarily, first 2 modes important to predict static aeroelastic deflection

## Slide 83
FE Model: Mode Shapes Wing/Body/Tail=0˚
Mode 1: 38.979 Hz
Mode 2: 40.401 Hz

## Slide 84
Mode 1: 38.991 Hz
Mode 2: 40.432 Hz
FE Model: Mode Shapes Wing/Body

## Slide 85
Full aircraft model with ~ 4 million DoFs
  Linear tetrahedral solid elements, bushing springs and kinematic rigid body elements
Linear static analysis during FSI
Pressure and wall shear from CFD++ transferred to CSM++ using nearest-neighbor interpolation
Computed deformations sent back to MetaFSI for mesh morphing
Repeat till displacements converge to within a tolerance of 1x10-6
Simulation Strategy

## Slide 86
CFD++ used a mirrored Medium Baseline NoQ Re=30M grid
  164,065,758 x 2 = 328,131,516 cells
Start with a steady-state “rigid” CFD++ run
Restart to begin coupled aero-structural analysis
Run CFD++ for 100 steps between each CFD-CSM coupling step
SARC-QCR turbulence model requires recomputing wall distance function after every FSI iteration
Simulation Strategy

## Slide 87
Converging to a solution…
Notes: Between 15 and 20 FSI iterations depending on the case

## Slide 88
Results: Deflected 50%-chord line

## Slide 89
Results: Deflected 50%-chord line

## Slide 90
Results: Wing Bending Deformation

## Slide 91
Results: Wing Bending Deformation

## Slide 92
Results: Wing Bending Deformation

## Slide 93
Results: Wing Bending Deformation

## Slide 94
Results: Wing Bending Deformation
Notes: Sting corrections???

## Slide 95
Results: Total Wing Twist

## Slide 96
Results: Total Wing Twist

## Slide 97
Results: Wing Twist Deformation

## Slide 98
Results: Wing Twist Deformation

## Slide 99
Results: Wing Twist Deformation

## Slide 100
Results: Wing Twist Deformation

## Slide 101
Wing Deformations, visualized

## Slide 102
α = 2.87˚
(CL = 0.58)
α = 3.25˚
α = 3.50˚
α = 3.75˚
α = 4.00˚
α = 4.25˚
Wing Deformations, visualized

## Slide 103
NoQ
LoQ 3.00˚
LoQ 3.25˚
LoQ 3.50˚
LoQ 3.75˚
LoQ 4.00˚
LoQ 4.25˚
Comparison with “LoQ” grids

## Slide 104: Summary
Good convergence for SARC+QCR, SST more problematic
SARC+QCR captures experimentally-observed pitch-break
  SST showed bifurcating solution & larger juncture separation
Juncture-region separation pattern not mesh converged
Shock-induced separation and body vortex footprint clear and unequivocal in all cases, but…
  Wing-vortex eye structure ambiguous in several runs
Coupled aero/structural model predicted deflections reasonably well (after matching q/E)
  Some discrepancies on length of deflected wings w.r.t. committee grids

## Slide 105
Thank you 

## Slide 106: Extra Slides : Comparison of Juncture-Region Wing Separation for cases 2a and 6

## Slide 107: Juncture-Region Wing Separation
Case 2a: α=3.25˚ 3.25˚ LoQ AE CRM geometry
Case 6: α=3.25˚
q/E=0.334 x10-6

## Slide 108: Juncture-Region Wing Separation
Case 2a: α=3.50˚ 3.50˚ LoQ AE CRM geometry
Case 6: α=3.50˚
q/E=0.334 x10-6

## Slide 109: Juncture-Region Wing Separation
Case 2a: α=3.75˚ 3.50˚ LoQ AE CRM geometry
Case 6: α=3.75˚
q/E=0.334 x10-6

## Slide 110: Juncture-Region Wing Separation
Case 2a: α=4.00˚ 3.50˚ LoQ AE CRM geometry
Case 6: α=4.00˚
q/E=0.334 x10-6

## Slide 111: Juncture-Region Wing Separation
Case 2a: α=4.25˚ 3.50˚ LoQ AE CRM geometry
Case 6: α=4.25˚
q/E=0.334 x10-6