## Slide 1: Kestrel Dual-Mesh Simulations for DPW-VII: Expanding the Envelope
Brent Pomeroy
NASA Langley Research Center
Configuration Aerodynamics Branch
CFD Drag Prediction Workshop VII
2022 AIAA AVIATION Forum
June 25-26, 2022

## Slide 2: Outline
Kestrel Overview and Compute Environment
Grids and Computational Methodology
Selected Cases
  Case 1a: Grid Convergence Study
  Case 2a: Alpha Sweep
  Case 3: Reynolds Number Sweep
  Case 4: RANS Grid Adaptation
  Case 5: Beyond RANS (DDES with Grid Adaptation)
  Extra credit interspersed throughout various Cases
Conclusions

## Slide 3: Kestrel CFD Solver
High-fidelity code from Department of Defense CREATE-AV
  Multidisciplinary tool that couples aerodynamics, S&C, thermochemistry, and propulsion
  Cell centered
  Includes RANS, URANS, and DDES schemes
  Alpha-seeking for local time stepping
  Alpha and CL seeking for global time stepping
Inner/outer dual-mesh approach
  Static inner unstructured grid
  Static or adaptive offbody Cartesian grid
  Unstructured grid trimmed at constant distance
Executed with Kestrel 12.1 SDK
Inner Unstructured Grid
Outer Cartesian Grid

## Slide 4: Supercomputing Environment
Executed on NASA Advanced Supercomputing (NAS) facility
  Comprised of four different supercomputers (Pleiades, Electra, Aitken, and Endeavour)
  More than 11,000 nodes and 241,000 compute cores
  Contains both Intel and AMD chips; TOSS3 (Linux 3) operating system
Resource usage for DPW-VII
  Intel Skylake nodes on Electra (a few select jobs on Haswell)
  Between 1,600 and 3,200 processors
  Walltime from a few hours to days
Total of 216 simulations
  Well in excess of 30 requested jobs for Cases 1a, 2a, 3, 4, and 5
  Large number of runs due to significant additional investigation and alpha-searching

## Slide 5: Grid Overview (1/2)
Committee-supplied JAXA unstructured grids
Variety of aeroelastic deformations
Six different grid densities
 | Tiny | Coarse | Medium | Fine | Extra Fine | Ultra Fine
Level | L1 | L2 | L3 | L4 | L5 | L6
Approximate Cell Count | 8.7 x 106 | 26.9 x 106 | 60.2 x 106 | 111.8 x 106 | 184.1 x 106 | 291.2 x 106
Tiny
Ultra Fine

## Slide 6: Grid Overview (1/2)
Committee-supplied JAXA unstructured grids
Variety of aeroelastic deformations
Six different grid densities
 | Tiny | Coarse | Medium | Fine | Extra Fine | Ultra Fine
Level | L1 | L2 | L3 | L4 | L5 | L6
Approximate Cell Count | 8.7 x 106 | 26.9 x 106 | 60.2 x 106 | 111.8 x 106 | 184.1 x 106 | 291.2 x 106
Tiny
Ultra Fine
 | Fully Unstructured | Adaptive Unstructured | Fixed Cartesian | Adaptive Cartesian
Case 1a | ✓ |  | ✓ | 
Case 2a |  |  | ✓ | 
Case 3 |  |  | ✓ | 
Case 4 |  |  |  | ✓
Case 5 |  |  |  | ✓

## Slide 7: Grid Overview (2/2)
Mixed element surface and volume grid
Surface grid made of quadrilaterals and triangles
Volume grid included tetrahedron, pyramids, prisms, and hexahedron
Surface
Red: quadrilaterals and triangles
Volume
Gray: tetrahedron
Gold: pyramids
Green: prisms
Brown: hexahedron

## Slide 8: Solution Setup
Computational approach
  HLLE++ inviscid flux and LDD+ viscous flux
  Second-order spatial and temporal accuracy
  Temporal damping applied to inner and outer grid
  Fully-turbulent SARC-QCR (QCR2000)
KCFD (inner solver) and SAMAir (outer solver)
Executed all RANS cases to 20,000 iterations, regardless of convergence behavior
Appreciation extended to the Committee for accelerating development of the reduction scripts and data file format

## Slide 9: Case 1a: Unstructured Grid Convergence
Simulations executed on all six densities
Data averaged over last 2,000 iterations
  From user’s best practices; may need more analysis
  More stable grid convergence for coarser grids
  Variations in CL consistent with typical Kestrel results
Mach 0.85
Re = 20 million
CL = 0.58

## Slide 10: Case 1a: Unstructured Grid Convergence
Simulations executed on all six densities
Data averaged over last 2,000 iterations
  From user’s best practices; may need more analysis
  More stable grid convergence for coarser grids
  Variations in CL consistent with typical Kestrel results
Excellent grid convergence with increasing density

## Slide 11: Case 1a: Inboard Pressure Cuts
Only minimal differences seen in inboard-most CP cuts
Largest differences seen at inboard cut trailing edge
  Region of interest for SOB separation region
  Grid density has a large effect on the junction flow
Moderate deviations near the leading edge lower surface
Decreased differences outside of junction flow region (Cut 5 plotted)

## Slide 12: Case 1a: Midspan and Outboard Pressure Cuts
Few differences seen in shock strength or location for the midspan and outboard locations (Cuts 9 and 12 representative of all results)
Minimal variations seen in trailing edge behavior (Cut 12 is representative)

## Slide 13: Case 1a: Overset Computational Domain
Inner-most Cartesian cell size of outer unstructured cell (best practice)
Outer box extends ~110 cref in all directions
Cartesian growth rate automatically determined

## Slide 14: Case 1a: Trim Distance Study
Nearbody grids trimmed using carp
  Kestrel’s grid manipulation package
  Supports numerous grid formats (including ugrid)
  Inner grid trimmed at a range of distances
Simulations were executed at constant 𝛼 (2.758 deg.) with minimal difference in drag or convergence
Selected trim
distance (0.06)

## Slide 15: Case 1a: Trimmed Grid Visualization
Selected 0.06
Close trim distance can lead to erroneous results and solution instability
Largely isotropic cell spacing at selected distance
Trim distance held constant for subsequent solutions

## Slide 16: Case 1a: Aerodynamic Performance
Alpha sweep executed on tiny and medium/trimmed (baseline) grids
  Sweep from 𝛼 of 0 to 8 deg. shown every 0.25 deg. (total of 86 jobs)
  Tiny grid yields decreased 𝛼pitchup and deeper CM bucket (not shown)
Difference in inboard flow separation ~0.50 deg.
Deviations observed in deep stall region

## Slide 17: Case 1a: Aerodynamic Performance
Alpha sweep executed on tiny and medium/trimmed (baseline) grids
  Sweep from 𝛼 of 0 to 8 deg. shown every 0.25 deg. (total of 86 jobs)
  Tiny grid yields decreased 𝛼pitchup and deeper CM bucket (not shown)
Difference in inboard flow separation ~0.50 deg.
Deviations observed in deep stall region
CD differences ~2.2 counts at 𝛼 of 3.00 deg.
(deg.)

## Slide 18: Case 1a: Computational Cost
Total cost for medium-density mesh
  Fully unstructured grid
  Trimmed grid at 0.06
1600 CPUs (40 Skylake nodes)
About 10.5 hours total for overset formulation
Cost per iteration is primarily between 2 and 4 sec. (without refinement)
Overset solution yields ~50% reduction in computational cost relative to unstructured

## Slide 19: Case 1a: Medium Trimmed Grid Alpha Sweep
Pitch break at ~3.0 deg. (CL ~0.62)
Inboard wing separation at ~7.25 deg.
2.50 deg.
2.75 deg.
3.00 deg.
3.25 deg.
Trailing Edge
Separation
CF
(deg.)
(deg.)

## Slide 20: Case 2a: Polar
Executed with medium grid and appropriate aeroelastic deformations
Increasing flow separation observed for 𝛼 > ~3.0 deg.
Progressive decambering leads to monotonically-decreasing CL𝛼 slope
Pitching moment break observed near CL ~0.62
(deg.)

## Slide 21: Case 2a: Inboard Surface Cuts
Increasing angle of attack yields a downstream shift in shock location
Shock clearly evidenced by CP and CF
Flow nominally attached downstream of the shock
Decelerated flow seen at trailing edge

## Slide 22: Case 2a: Mid-Span Surface Cuts
Downstream shift in shock observed with larger angles of attack (expected)
No double shocking at high angles
Flow separates at shock location and fails to reattach above 𝛼 = 3.25 deg.

## Slide 23: Case 3: Reynolds Number Sweep
Executed on LoQ and HiQ lofts at CL = 0.50
Significant drag rise with decreased Re (expected)
Large drag rise seen from Re of 20 million to 5 million (expected)
(deg.)

## Slide 24: Case 4: RANS Adaptive Mesh
Adaptive mesh refinement performed in offbody Cartesian grid
  Nearbody-grid adaptation not yet available
  User-specified region limits shown in blue box
  Amount of refinement based upon a threshold value
  Separated wake led to decision to refine based on ω
Refinement applied every 250 iterations
Adaptation used over the entire simulation (not frozen)
Grid density must be traded with computational cost

## Slide 25: Case 4: Effect of Refinement Threshold (1/3)
Threshold value controls degree of grid refinement based on values of ω
  Decreased threshold yields increased grid density
  Cases run at threshold values from 40 through 200 (12 jobs total)
  Executed for 6,000 iterations – sufficient to understand grid resolution
  Cartesian grid convergence observed after 5,000 iterations
Analysis performed at 𝛼 = 2.75 deg. (plotted) and 4.25 deg.
2.75 deg.
2.75 deg.
Increasing
Density

## Slide 26: Case 4: Effect of Refinement Threshold (2/3)
Selection of threshold significantly affects wake refinement
Chose threshold value of 60 with ~280 million cells in Cartesian region
  Minimal grid changes at 𝛼 = 2.75 deg.
  Adequately captures wing tip vortex, mid-span separation, and fuselage vortex
2.75 deg. thresh=60
2.75 deg. thresh=200
4.25 deg. thresh=60

## Slide 27: Case 4: Effect of Refinement Threshold (3/3)
Range of thresholds analyzed at CL of 0.58
Threshold value has minimal effect on F&M at this condition
  Consistent with expected results
  Improved resolution of the wake and the shock
This observation does not mean that refinement has no effect on the global F&M (covered in next slides)

## Slide 28: Case 4: Aerodynamic Performance
Adapted grid yields only a slight reduction in lift and moment magnitude
Pitch-up break point extremely similar for both formulations
Observations consistent with typical Kestrel behavior
(deg.)
(deg.)

## Slide 29: Case 4: Convergence History
Similar convergence history across full range
Differences in averaged values
  Grid-adapted solutions yield decreased drag
  CL ~0.001
  Maximum CD delta ~3 counts
𝛼

## Slide 30: Case 4: Pressure Cuts (CL 0.58)
Overall, minimal changes observed in surface CP data
Slight forward movement of shock at outboard locations

## Slide 31: Case 5: Beyond RANS (DDES Adaptive Mesh)
Similar setup to RANS cases
  Same refinement region and settings
  SARC-QCR turbulence model
Averaging window
  Simulation run for 26,000 iterations (not 20,000)
  Began averaging at 20,000 iterations
  Averaged for 6,000 iterations (not 2,000)
Nondimensional time step set to 0.010, dimensional time step falls out

## Slide 32: Case 5: Beyond RANS (DDES Adaptive Mesh)

## Slide 33: Case 5: Opportunities for Investigation
A more thorough investigation is warranted
Grid considerations
  Appropriateness of current grids for DDES need to be investigated
  Possibility of modeled stress depletion should be analyzed
Computational settings
  Temporal damping may need to be considered
  Examine impact of RC and QCR
  Smaller time steps might be significant

## Slide 34: Summary
Analysis performed on Cases 1a, 2a, 3, 4, and 5
Excellent unstructured grid convergence achieved
Pitch break observed CL ~0.62
Offbody adaptive mesh refinement improved wake prediction, but minimal effect on integrated F&M
Unsteady DDES yielded earlier separation than RANS

## Slide 35: Questions?